## Slide 1
ARP
The Address Resolution Protocol
Who are we ARPing for?
or
Who for ARP thou?

## Slide 2
Note to Reader
The information explained in this section is a simplification and extrapolation of the actual ARP determination process.
Although conceptually accurate, the actual process is slightly different and more complex.
However, for the purposes of this curriculum, the explanation contained in this section provide a good basis of understanding.

## Slide 3
First, a quick review...
ARP is a layer 3 protocol, one of many protocols within the TCP/IP suite of protocols.

## Slide 4
Why do devices need to map a MAC Address to an IP Address?
Host Stevens
172.16.10.10
255.255.255.0
MAC 00-0C-04-17-91-CC
172.16.10.0/24
Host Cerf
172.16.10.25
255.255.255.0
MAC 00-0C-04-38-44-AA
ARP Table
IP Address
MAC Address
172.16.10.3
00-0C-04-32-14-A1
172.16.10.19
00-0C-14-02-00-19
172.16.10.33
00-0C-A6-19-46-C1
Destination
Source
Destination MAC Address???
Router A
Ethernet 0
172.16.10.1
255.255.255.0
MAC 03-0D-17-8A-F1-32

## Slide 5
Devices, (hosts, routers, servers, etc.) use IP addresses to reach other devices within their own network/subnet or across different networks/subnets.
Layer 3 addresses such as IP addresses, include a source address of the sending device and the destination address of the intended recipient.
In other words the IP addresses consist of the original source address and final destination address.

## Slide 6
Data Link addresses, such as Ethernet MAC addresses are used to get the IP packet from one hop to the next.
You may wish to review the section on Encapsulation and Routers for more clarification.

## Slide 7
Why do devices need to map a MAC Address to an IP Address?
The simple answer is deliver the IP packet inside an Ethernet frame to the next hop along the way. The next hop may very well be the final destination.
To better explain this, lets use a couple of examples.

## Slide 8
Host Stevens
172.16.10.10
255.255.255.0
MAC 00-0C-04-17-91-CC
172.16.10.0/24
Host Cerf
172.16.10.25
255.255.255.0
MAC 00-0C-04-38-44-AA
Destination
Source
Router A
Ethernet 0
172.16.10.1
255.255.255.0
MAC 03-0D-17-8A-F1-32
Here we have an example of Host Stevens at IP address 172.16.10.10 wanting to send an IP packet to Host Cerf at IP address 172.16.10.25.
Example 1: Two devices (hosts) are on the same subnet

## Slide 9
Host Stevens needs to send this packet either:
a) directly to the final destination, Host Cerf
or
b) the default gateway, the router, so it can forward it onward
  How does Host Stevens know where it needs to send this packet?

## Slide 10
Depending upon the answer, Host Stevens will either look for Host Cerf’s IP address of 172.16.10.25 in its ARP table or that of the default gateway, Router A’s IP address of 172.16.10.1
This is the “big question!”

## Slide 11
The BIG Question
Which IP address does the sending host (Stevens) look for in its ARP table? And if that IP address is not there, which IP Address does it send an ARP Request for?
Is it:
The IP Address of the destination host?
The IP Address of the default gateway (the router)?

## Slide 12
The Answer
It depends on whether the final destination address is on its same subnet or that of a different subnet or network.
The sending host must determine whether the final destination IP address is on the same subnet as itself.

## Slide 13
Same Subnet
If the final destination is on the same subnet as the sender, then it knows it can send the packet directly to the final destination.
It will look up the final destination IP address in its ARP table for the MAC address.
If the IP address is in the ARP table it will encapsulate the IP packet into the Ethernet frame.
The sender will use the MAC address it got from the ARP table for the Destination MAC address in the Ethernet frame.

## Slide 14
If the IP address is not in the ARP table the sender will need to send out an ARP Request in order to get the MAC address.

## Slide 15
Example 1: Two hosts are on the same subnet
Host Stevens
172.16.10.10
255.255.255.0
MAC 00-0C-04-17-91-CC
172.16.10.0/24
Host Cerf
172.16.10.25
255.255.255.0
MAC 00-0C-04-38-44-AA
Destination
Source
Router A
Ethernet 0
172.16.10.1
255.255.255.0
MAC 03-0D-17-8A-F1-32
Host Stevens at IP address 172.16.10.10 wants to send an IP packet to Host Cerf at IP address 172.16.10.25.

## Slide 16
The sender, Host Stevens, compares its IP Address with the destination host’s IP Address, using the sender’s (Host Stevens’) subnet mask to extract the network portion for both IP Addresses.
By doing AND operations on both IP Addresses, host Stevens determines whether or not both hosts are on the same network/subnet.

## Slide 17
Host Stevens IP Address 172.16.10.10
Host Stevens Subnet Mask 255.255.255.0
------------------------- --------------
Host Stevens Network 172.16.10.0
Host Cerf IP Address 172.16.10.25
Host Stevens Subnet Mask 255.255.255.0
------------------------- --------------
Host Cerf Network 172.16.10.0

## Slide 18
Notice that Host Stevens uses its own subnet mask which defines which subnet it is directly connected to.
So, when doing the AND operation, it uses its own subnet mask for both AND operations.

## Slide 19
Host Stevens determines that it belongs to the 172.16.10.0 subnet and that Host Cerf is also on the 172.16.10.0 subnet.
Same subnet!
This means that Host Stevens can send the packet directly to Host Cerf.
Now, that Host Stevens knows that Host Cerf is on its same subnet, all that is left is for Host Stevens to look up Host Cerf’s IP address in its ARP table, in order to get the Host Cerf’s MAC address, so it can encapsulate the IP packet in the Ethernet frame and send it directly to Host Cerf.

## Slide 20
Host Stevens
172.16.10.10
255.255.255.0
MAC 00-0C-04-17-91-CC
172.16.10.0/24
Host Cerf
172.16.10.25
255.255.255.0
MAC 00-0C-04-38-44-AA
ARP Table
IP Address
MAC Address
172.16.10.3
00-0C-04-32-14-A1
172.16.10.19
00-0C-14-02-00-19
172.16.10.33
00-0C-A6-19-46-C1
Destination
Source
Destination MAC Address???
Router A
Ethernet 0
172.16.10.1
255.255.255.0
MAC 03-0D-17-8A-F1-32
Host Stevens checking its ARP table for Host Cerf’s MAC address...

## Slide 21
In the example above, Host Cerf’s IP Address does not appear in Host Stevens’ ARP Table.
Host Stevens must send out an ARP Request for the IP address 172.16.10.25, Host Cerf’s IP address.
Once again, Host Stevens knows it can do an ARP request directly for Host Cerf, because it had determined they are both on the same subnet.

## Slide 22
Let’s do the ARP Request
Note: You may wish to skip this part if you do not need the review.
So, what does an ARP packet look like?

## Slide 23
ARP Request from Host Stevens at 172.16.10.10
op field – ARP request = 1
ARP reply = 2
RARP request = 3
RARP reply = 4
“Hey everyone! I have this IP Address and I need
the host this belongs to, to send me their MAC
address.”

## Slide 24
“Hey sender of ARP Request! Here is my MAC address that you wanted for that IP address.”
Here it is!
ARP Reply from Host Cerf at 172.16.10.25

## Slide 25
Host Stevens receives the ARP Reply and enters Host Cerf’s IP address and MAC address into its ARP Table.
Host Stevens now has all it needs to encapsulate the IP packet into the Ethernet frame and send that packet directly to Host Cerf.

## Slide 26
Example 2: Two hosts are on different subnets
Here we have an example of Host Stevens at IP address 172.16.10.10 wanting to send an IP packet to Host Perlman at IP address 172.16.20.12
Host Stevens
172.16.10.10
255.255.255.0
MAC 00-0C-04-17-91-CC
172.16.10.0/24
Host Perlman
172.16.20.12
255.255.255.0
MAC 00-0C-22-A3-14-01
Destination
Source
Router A
Ethernet 0
172.16.10.1
255.255.255.0
MAC 03-0D-17-8A-F1-32
172.16.20.0/24

## Slide 27
Host Stevens needs to send this packet either:
a) directly to the final destination, Host Perlman
or
b) the default gateway, the router, so it can forward it onward
How does Host Stevens know where it needs to send this packet?

## Slide 28
Depending upon the answer, Host Stevens will either look for Host Perlman’s IP address of 172.16.20.12 in its ARP table or that of the default gateway, Router A’s IP address of 172.16.10.1
This is the “big question!”

## Slide 29
The BIG Question
Which IP address does the sending host (Stevens) look for in its ARP table? And if that IP address is not there, what IP Address does it send an ARP Request for?
Is it:
The IP Address of the destination host?
The IP Address of the default gateway (the router)?

## Slide 30
The Answer
It depends on whether the final destination address is on its same subnet or that of a different subnet or network.
The sending host must determine whether the final destination IP address is on the same subnet as itself.

## Slide 31
Different Subnet
If the final destination is on a different subnet then the sender knows it can not send the packet directly to the final destination.
Instead, the sender will look up the IP address of the default gateway.
This is why hosts normally have not only an IP address and subnet mask, but also an IP address of a default gateway.

## Slide 32
The default gateway is usually a router, which hosts send packets to when the destination IP address is on a different subnet or network.
The sender will look up the default gateway’s IP address in its ARP table for the MAC address of the default gateway.
If the IP address is in the sender’s ARP table it will encapsulate the IP packet into the Ethernet frame and send the packet to the default gateway (i.e. the router).

## Slide 33
If the IP address is not in the ARP table the sender will send an ARP Request for the MAC address of the default gateway (i.e. the router).

## Slide 34
Lets see how it does this by using our example.
Here we have an example of Host Stevens at IP address 172.16.10.10 wanting to send an IP packet to Host Perlman at IP address 172.16.20.12
Host Stevens
172.16.10.10
255.255.255.0
MAC 00-0C-04-17-91-CC
172.16.10.0/24
Host Perlman
172.16.20.12
255.255.255.0
MAC 00-0C-22-A3-14-01
Destination
Source
Router A
Ethernet 0
172.16.10.1
255.255.255.0
MAC 03-0D-17-8A-F1-32
172.16.20.0/24

## Slide 35
The sender, Host Stevens, compares its IP Address with the destination host’s IP Address, using the sender’s (Host Stevens’) subnet mask to extract the network portion for both IP Addresses.
By doing AND operations on both IP Addresses, host Stevens determines whether or not both hosts are on the same network/subnet.

## Slide 36
Host Stevens IP Address 172.16.10.10
Host Stevens Subnet Mask 255.255.255.0
------------------------- --------------
Host Stevens Network 172.16.10.0
Host Perlman’s IP Address 172.16.20.12
Host Stevens Subnet Mask 255.255.255.0
------------------------- --------------
Host Perlman’s Network 172.16.20.0

## Slide 37
Notice that Host Stevens uses its own subnet mask which defines which subnet it is directly connected to.
So, when doing the AND operation, it uses its own subnet mask for both AND operations.

## Slide 38
Host Stevens determines that it belongs to the 172.16.10.0 subnet and that Host Perlman is on the 172.16.20.0 subnet.
Different subnets!
This means that Host Stevens can not send the packet directly to Host Perlman.
Now, that Host Stevens knows that Host Cerf is on a different subnet, it knows that it must send the packet to the default gateway, the router.
Host Stevens will look up the default gateway’s IP address (which has been entered by the user or received by a DHCP server), in its ARP Table.

## Slide 39
Host Stevens checking its ARP table for the router’s MAC address...
Host Stevens
172.16.10.10
255.255.255.0
MAC 00-0C-04-17-91-CC
172.16.10.0/24
Host Perlman
172.16.20.12
255.255.255.0
MAC 00-0C-22-A3-14-01
ARP Table
IP Address
MAC Address
172.16.10.3
00-0C-04-32-14-A1
172.16.10.19
00-0C-14-02-00-19
172.16.10.33
00-0C-A6-19-46-C1
Destination
Source
Default Gateway's (the router's)
MAC Address???
Router A
Ethernet 0
172.16.10.1
255.255.255.0
MAC 03-0D-17-8A-F1-32
172.16.20.0/24

## Slide 40
In the example above, Host Perlman’s IP Address does not appear in Host Stevens’ ARP Table.
Host Stevens must send out an ARP Request for the IP address 172.16.10.1, Router A’s IP address.
Host Stevens can not do an ARP request directly for Host Perlman, because it had determined they are on different subnets.

## Slide 41
Let’s do the ARP Request
Note: You may wish to skip this part if you do not need the review.
So, what does an ARP packet look like?

## Slide 42
“Hey everyone! I have this IP Address, 172.16.10.1, and I need the device this belongs to, to send me their MAC address.”
op field – ARP request = 1
ARP reply = 2
RARP request = 3
RARP reply = 4
ARP Request from Host Stevens at 172.16.10.10

## Slide 43
“Hey sender of ARP Request! Here is my MAC address that you wanted for that IP address.”
Here it is!
ARP Reply from Router A at 172.16.10.1

## Slide 44
Host Stevens receives the ARP Reply and enters Router A’s IP address and MAC address into its ARP Table.
Host Stevens now has all it needs to encapsulate the IP packet into the Ethernet frame and send that packet to Router A.

## Slide 45
It is now up to Router A to forward the packet onward.